## Slide 1
Real Time Device to Device Wireless Communication System Using ESP-NOW Protocol
Abdul Rehman
Registration No: 0000674917 | Program: BSCS
Supervisor: Israr Akhter
Dual Mode Severity Classification: DBMS Decision Matrix and On Device TinyML Inference
Phase 4
Total Time
15-20 Minutes

## Slide 2: Background
Phase 1
Wireless sensing link
Two NodeMCU (ESP8266) boards paired over ESP-NOW. A Sender on a small car carries an ultrasonic sensor and a PIR motion sensor and transmits a confirmed detection to a Receiver.
Phase 2
Database and dashboard
The Receiver forwards each confirmed detection over WiFi to a PHP script, which stores it in a MySQL database. A web dashboard renders the stored data for review.
Phase 3
Rule based intelligence
A distance based severity zone and a timing pattern anomaly check are combined by a deterministic decision matrix on the server, with results shown and exportable on the dashboard.
Phase 4
Dual mode classification
A physical switch lets each board choose between the Phase 3 server decision matrix and a Decision Tree Classifier running as embedded C++ inference directly on the microcontroller.
CURRENT PHASE

## Slide 3: Introduction to Phase 4 and Problem Statement
The system uses two ESP8266 boards, a Sender on a moving car and a Receiver at a fixed point.
The Sender reads an ultrasonic sensor and a motion sensor, then reports detections wirelessly using ESP-NOW.
The Receiver forwards data to a MySQL database and a live dashboard.
Problem: severity in Phase 3 was decided only on the server, so the reaction always waited on the network.
Problem in one line: network delay stood between sensor detection and physical warning.
Sender
(Car)
Receiver
(Fixed)
MySQL Server
+ Dashboard
ESP-NOW
WiFi + HTTP

## Slide 4: Objectives
Let each board choose DBMS mode or TinyML mode using a switch
Train a Decision Tree model and run it directly on ESP8266
Redesign Sender sampling for fast, moving object detection
React instantly with buzzer and LED in TinyML mode
Log every on device prediction separately from server data
Show model accuracy and live predictions on the dashboard

## Slide 5: Scope of This Phase
Sender Firmware | One second sampling cadence, glitch rejecting recheck, distance based duplicate suppression, and a mode switch controlling local prediction.
Receiver Firmware | Independent mode switch, buzzer and severity LED, and two mode exclusive reaction paths: server forwarding or local Decision Tree inference.
Offline training pipeline | scikit-learn Decision Tree trained on labeled detection data; micromlgen exports it to shared C++ source for both boards.
Synthetic test data | A clearly labeled generator producing balanced volume so the dashboard, its filters, and the trained model can be demonstrated and evaluated.
New database table | tinyml_predictions and a dedicated log_tinyml_result.php, kept structurally separate from detection_events and the DBMS pipeline.
Dashboard additions | A Machine Learning page showing offline training performance and a live, filterable, exportable log of on device predictions.

## Slide 6: System Overview and Dual Mode Architecture
Each board decides on its own, DBMS mode or TinyML mode, using a physical switch.
DBMS MODE
Receiver sends data to server
PHP script computes final status
Distance zone plus pattern anomaly
Needs WiFi and server availability
TINYML MODE
Decision Tree runs on the chip itself
No server call needed for reaction
Buzzer and LED react immediately
Prediction logged later, best effort

## Slide 7: On Device Decision Tree Classifier
Trained offline with scikit-learn on three features already produced by the pipeline, then exported to plain C++ with micromlgen so both boards run an identical, dependency free model.
Distance: Ultrasonic reading in centimetres
Interval: Seconds since the previous confirmed detection
Pattern anomaly: Flag inherited unchanged from Phase 3
Target label: final_status (normal, warning, critical). Maximum tree depth capped at five so the exported C++ stays small and fast on an ESP8266.
RESULT
The tree splits only on distance
at 7.5 cm and 14.5 cm, the same boundaries as the Phase 3 severity zones, and never branches on interval or the anomaly flag.
Why: the synthetic training labels assign final_status purely from distance zone, with no exception for a pattern anomaly, so interval and anomaly carry no information the tree can use.
Both extra features stay in the predict signature, ready for a future retraining pass on labels that let the anomaly flag influence the target.

## Slide 8: Hardware Components
Component | Purpose
NodeMCU ESP8266 | Sender and Receiver boards
PIR Motion Sensor | Confirms real movement nearby
Ultrasonic Sensor | Measures distance to object
LEDs | Show mode and status visually
Buzzer | Sounds warning and critical alerts
Mode Switch (per board) | Selects DBMS or TinyML mode

## Slide 9: Software and Technologies Used
Firmware
Arduino C++
ESP-NOW Protocol
Backend
PHP
MySQL Database
Machine Learning
Python
scikit-learn
micromlgen (C++ export)
Dashboard
HTML
JS
Chart.js

## Slide 10: Working Methodology
This cadence replaced the old fixed wait time, so a moving object is reported right away.
DBMS Path
Data goes to server. Server checks distance zone and timing pattern together, then returns final status.
TinyML Path
Decision Tree on the chip checks distance directly, and the buzzer or LED reacts within milliseconds.
Sample sensors every 1 second
Recheck once to reject noise glitch
Compare with last reported distance
Send new reading over ESP-NOW
Receiver checks its own mode switch
Server or on device model decides

## Slide 11: NETWORKING Sender to Receiver Link — ESP-NOW Protocol
Function: carry a confirmed detection from the car to the fixed Receiver, with minimum delay.
OSI Layers Used
Data Link Layer: MAC level action frames carry the payload
Physical Layer: 2.4 GHz WiFi radio, no access point needed
Why ESP-NOW Was Chosen
No pairing or router needed between the two boards
Very low latency, well suited to real time alerts
Works using known MAC addresses directly
Alternative Protocols Considered and Why Not Used
Regular WiFi + TCP/IP: Needs a router, adds connection setup delay and more power use
Bluetooth / BLE: Shorter reliable range, pairing overhead not needed here
Zigbee: Needs an extra radio module and mesh setup for just two nodes
LoRa: Long range but low data rate and higher latency, not needed for a short link

## Slide 12: NETWORKING Receiver to Server Link — Full Protocol Stack
Function: carry confirmed data from the Receiver to the PHP and MySQL backend.
OSI Layers Used
Application Layer: HTTP request, JSON body, sent to receive_data.php
Transport Layer: TCP, guarantees ordered and reliable delivery
Network Layer: IP, gives the Receiver its local address
Data Link + Physical: 802.11 WiFi radio to the home router
Why This Stack Was Chosen
Matches the existing PHP and MySQL backend directly
JSON over HTTP is human readable and easy to debug
TCP reliability matters for permanent database writes
Alternative Protocols Considered and Why Not Used
UDP Faster but no delivery guarantee, needs custom retry code
MQTT Great for IoT, but needs a separate broker service to run
CoAP Built for constrained devices, not supported by the PHP backend

## Slide 13: DBMS Storing Detection Data — Relational Database Model
Function: keep every confirmed detection and prediction, in a form the dashboard can query and filter.
DBMS Concepts Applied
Primary keys uniquely identify each event and prediction
Foreign keys link sensor readings back to their parent event
ENUM constraints restrict severity and device role values
Normalization avoids repeating sensor data inside events
ACID properties keep writes consistent under concurrent access
Why Relational (MySQL) Was Chosen
Fields are fixed and well defined, distance, interval, severity
Events and readings need reliable joins for the dashboard
Mature tooling works cleanly with the existing PHP backend
Alternatives Considered
NoSQL document store: flexible schema not needed here
Firebase: adds a cloud dependency the local design avoids
Flat file logging: no indexed queries or joins for filtering

## Slide 14: DBMS Protecting the Database — Prepared Statements
Function: insert every detection and prediction safely, without exposing the database to attack.
Technique Used
Prepared statements through PHP mysqli
SQL code and user supplied data are kept separate
Sensor values are bound as parameters, never concatenated
Alternative Rejected
Direct string concatenated queries: Rejected because malformed or malicious sensor input could alter the query itself, opening a standard SQL injection path into the database.

## Slide 15: TINYML TinyML — The Main Contribution of Phase 4
TinyML means training a model on a full computer, then compressing it to run inference directly on a microcontroller with only kilobytes of memory.
Why this matters: in Phase 3, severity was known only after a full network round trip. TinyML removes that dependency entirely, the prediction and the physical reaction now happen on the microcontroller itself.
Train Offline
train_tinyml_severity.py fits a Decision Tree in scikit-learn on distance, interval, and anomaly flag
Export to C++
micromlgen converts the fitted tree into model.h, a small dependency free C++ class
Compile into Firmware
model.h is included directly in sender.ino and receiver.ino, no Python or library needed on chip
Infer on Chip
The Receiver calls predict() locally and reacts through the buzzer and Yellow LED, no server call

## Slide 16: TINYML On Device Prediction — TinyML Model Selection
Function: decide severity directly on the microcontroller, with no protocol round trip at all.
Model Used
scikit-learn Decision Tree Classifier, max depth of five
Trained offline on distance, interval, and anomaly flag
Exported to plain C++ with micromlgen, no dependencies
Runs the same trained tree on both Sender and Receiver
Why Decision Tree Was Chosen
Small memory footprint, fits easily in ESP8266 flash
No runtime interpreter needed at prediction time
Fast inference for a simple three feature problem
Alternative Rejected
Neural network with TensorFlow Lite Micro: Needs a runtime interpreter and more flash and RAM than a three feature, three class problem actually requires.

## Slide 17: Summary One Function, One Subject, One Justified Choice
Function | Subject | Chosen Approach | Main Alternative Rejected
Sender to Receiver link | Computer Networks | ESP-NOW (OSI L1-L2) | WiFi, Bluetooth, Zigbee, LoRa
Receiver to Server link | Computer Networks | WiFi + TCP/IP + HTTP | UDP, MQTT, CoAP
Detection data storage | Database Management System | MySQL relational model | NoSQL, Firebase, flat file
Insert query safety | Database Management System | Prepared statements | String concatenated SQL
On chip severity prediction | TinyML | Decision Tree + micromlgen | Neural net + TFLite Micro
Each row uses the vocabulary of its own subject, networking terms for links, DBMS terms for storage, and TinyML terms for on chip prediction. |  |  | 

## Slide 18: Implementation: Circuit and Code Overview
Circuit Setup
Sender: ultrasonic + PIR sensor, mode switch on pin D4
Receiver: buzzer + 3 LEDs, mode switch on pin D7
Internal pull up resistor used, so no extra resistor needed
Green/Red LEDs for DBMS mode, Yellow LED for TinyML mode
Code Overview
sender.ino: reads sensors, runs model.h if TinyML mode
receiver.ino: sends to server or predicts locally
model.h: Decision Tree exported to plain C++
receive_data.php + log_tinyml_result.php

## Slide 19: Results and Live Demonstration
Dashboard shows live severity, sensor history, and model predictions.
Confusion matrix confirms every test row was classified correctly.
TinyML mode reacts through buzzer and LED, no server needed.
Live demo: switch modes on both boards and show instant reaction.
30,010
Confirmed Events
90.85%
Test Accuracy
18
Live Predictions Logged
63
Pattern Anomalies

## Slide 20: Challenges and Future Improvements
Challenges
Model only learned distance, not timing pattern
Perfect accuracy came from clean synthetic labels
Manual testing skewed pattern anomaly results
DBMS and TinyML labels are not fully comparable yet
Future Work
Retrain model on the same labels as server logic
Compare DBMS and TinyML results event by event
Run a longer test with a real moving object
Add database transactions for safer data saving
Evaluate Isolation Forest anomaly models formally

## Slide 21: CONCLUSION
This project built a real time obstacle detection system that can decide severity in two ways, through a server based decision matrix or through a Decision Tree running directly on the microcontroller.
Each function, from the wireless link, to the database, to the on chip model, was designed using the rules of its own subject and justified against real alternatives.
Both approaches remain clearly separated in the data, keeping the results honest and easy to compare.

## Slide 22
Thank You
Questions?
Real Time Device to Device Wireless Communication System Using ESP-NOW Protocol (Phase 4)
Abdul Rehman | BSCS | Allama Iqbal Open University